## Slide 1
The Great Salt Lake Summer Ozone Study
John Horel, Erik Crosman, Alex Jacques, Brian Blaylock, Ansley Long, University of Utah
Seth Arens, Utah Division of Air Quality; Randy Martin, Utah State University and John Sohl, Weber State University

## Slide 2: Why is ozone a concern along Wasatch Front?
Background ozone levels in the west are high and likely to increase
  Distant, regional, local emissions and transport
  Increased wildfires
Prior field & modeling studies by Utah Division of Air Quality (DAQ) indicated high ozone concen-trations over & near the Great Salt Lake
Wasatch Mountains
Great Salt Lake
Wasatch Front
Salt Lake
Valley

## Slide 3: Objectives of this pilot study…
Determine the distribution of ozone near the Great Salt Lake during summer
Improve understanding of the meteorological processes that control ozone concentrations over and surrounding the Lake during summer
Contribute to improved ozone forecasts by Utah DAQ

## Slide 4: Cost-effective pilot field study
Small budget from Utah DAQ leveraged by other funds
Used existing infrastructure in our own backyard to reduce costs
Real-time data collection and analysis: 1 June - 31 August 2015
Summer study allowed for more graduate & undergraduate student participation
Great Salt Lake Causeway

## Slide 5
Leveraging Existing Resources
Instruments | Resource
DAQ Fixed Site Ozone Monitors | DAQ Ozone Monitors - part of regular monitoring network
Temporary Fixed Site Ozone Monitors | DAQ and UofU temporary deployments, some adjacent to existing UofU weather stations and available in real-time
Weather Observations | MesoWest (http://mesowest.utah.edu) MesoWest API (http://mesowest.org/api)
Mobile Ozone Observations | UTA TRAX Light Rail Car (continuous) KSL-TV “Chopper” 5 (often late afternoon) UofU Nerdmobile (IOPs) UofU Additional Vehicles (IOPs)
Boundary Layer Air Quality Observations | USU UAV WSU Tethersonde
Boundary Layer Remote Sensing | UofU Sodars, Lidar, and Ceilometers
Real-time Ozone Measurements During the 2015 Great Salt Lake Summer Ozone Study
Jacques et al., Paper 7.2 18th Symposium on Meteorological Observation and Instrumentation

## Slide 6
DAQ Ozone Monitors
Temporary Ozone Monitors
MesoWest Sites
Sodars, Buoy, Lidar, Ceilometers,
UAV, Balloon
Fremont Island
Badger Island
Hawthorne

## Slide 7
Mobile Ozone Observations
Continuous real-time monitoring via instrument deployed on Utah Transit Authority (UTA) TRAX Light Rail Car
Intermittent deployment of mobile units with real-time cellular communications deployed in vehicles and on KSL-TV “Chopper 5” helicopter

## Slide 8
Mobile Observations
June-August 2015
Repeated Routes
TRAX
Red Line

## Slide 9
Chopper: Opportunistic flights
June-August 2015

## Slide 10
Real-Time Ozone Processing and Display
Data collected from logging devices in real-time
Processed into MesoWest database (fixed sites) or HDF5 (mobile)
Data synthesized on website: http://meso2.chpc.utah.edu/gslso3s

## Slide 11
Daily 8-h Maximum Ozone in Salt Lake Valley (Hawthorne) during summer
Station | # 2015 Summer Days > 70 ppb
Farmington Bay | 19
Salt Lake Valley (Hawthorne) | 18
Badger Island | 17
Saltaire | 16
Wildfire Smoke
Synoptic Ridge

## Slide 12: In-Situ Observations at 5-min intervals
Badger Island
Farmington Bay
Badger
Island
Farmington
Bay
1 Jun 15 Jun 1 Jul 15 Jul 1 Aug 15 Aug 1 Sep
1 Jun 15 Jun 1 Jul 15 Jul 1 Aug 15 Aug 1 Sep
Nocturnal titration reduced at remote Badger Island relative to Farmington Bay located between Lake and urban areas

## Slide 13: Ozone Roses: 1 June - 31 August
Badger
Island
Farmington
Bay
Badger Island Farmington Bay
Persistent cross-lake
easterly flow
Dominated by nocturnal land breezes and
Daytime lake breezes
(replace with daytime only one?)

## Slide 14
Ozone Rose
Notes: Now we’re going to look at some of the data we collected…
Ozone roses
Show the frequency of wind direction for each ozone interval of ozone concentration

## Slide 15: Intensive Observing Periods (IOPs) and Other Periods of Interest
Period | Conditions | Ozone (ppb) | Field Notes
3 June | Evening Thunderstorm | Over 70 ppb at Salt Lake Valley stations | June 3
17 June - 3 July | Ridging & hotter than normal | Peak ozone over 70 ppb somewhere every day | Chopper 5
IOP 1: 17 - 18 June | Strong lake breeze front on 18th | Ozone concentrated along frontal boundary aloft | IOP 1
IOP 2: 15 - 16 July | Well mixed, deep boundary layer up to 550 mb with afternoon convection | Peak concentrations barely exceeding 70 ppb | IOP 2
IOP 3: 10 -12 August | Monsoonal conditions | 8 h avg over 70 ppb in Salt Lake Valley | 14 August Daily Summary
16 - 24 August | Regional smoke transport | Elevated ozone and PM2.5 concentrations | Smoke Week
Next talk:
Brian Blaylock

## Slide 16
Wasatch Front: Crossroads of the Smoky West
15-24 August 2015
Cessation of summer monsoon; dry NW flow advected smoke from Pacific Northwest and California wildfires
Elevated ozone and particulate levels obscured visibility

## Slide 17
18 August: Chopper 5 asked to fly above smoke in boundary layer

## Slide 18
18- 19 August: Conditions on UU Campus on eastern side of Valley
Night
Night
Day
Day
NE
W
Blue: wind direction
Red: wind speed
Green: peak wind
Blue: PM 2.5
Chopper
flight

## Slide 19
18- 19 August: Conditions on UU Campus on eastern side of Valley
Night
Night
Day
Day
NE
W
Blue: wind direction
Red: wind speed
Green: peak wind
Ozone: PM 2.5
Chopper
flight

## Slide 20
18- 19 August: Conditions on UU Campus on eastern side of Valley
Night
Night
Day
Day
NE
W
Blue: wind direction
Red: wind speed
Green: peak wind
Black Carbon. Aethalometer provided by Sonoma Tech
Chopper
flight

## Slide 21
18- 19 August: Conditions on UU Campus on eastern side of Valley
Night
Night
Day
Day
NE
W
Blue: wind direction
Red: wind speed
Green: peak wind
Brown Carbon. Aethalometer provided by Sonoma Tech
Chopper
flight

## Slide 22: Summary
Even though a pilot study, the Great Salt Lake Summer Ozone Study was the most extensive field study ever undertaken related to summer air quality along the Wasatch Front
We utilized existing infrastructure, temporary deployments, and sensors on diverse mobile platforms
Real-time data collection and web displays helped us target how to collect the data as well as allow quick-look analyses
Access the data and preliminary analyses from meso2.chpc.utah.edu/gslso3s/
Notes: To conclude, we hope you take these points home with you…
Ozone is bad, and hopefully you realize that residents on the WF are exposed to unhealthy levels through the summer.
.
.
.
.

## Slide 23: Incompletely answered issues and questions
Wet spring on low-lying and hillside vegetation possibly leading to generation of biogenic ozone precursors
Early season shallow lake thermocline leading to shallow Lake boundary layer and higher ozone
Why were the highest ozone concentrations near the margins of the Lake rather than further offshore?
What was the influence of enhanced albedo from the exposed salt flats on ozone formation?
What are the direct and secondary roles of the Great Salt Lake on ozone production including chlorine chemistry?
How does the intensity and duration of nocturnal titration along the shores of the Great Salt Lake depend on other pollutants (NOX, etc.)?
How are the ozone concentrations affected by the relative strength, intensity, and timing of land and lake breezes compared to those of concurrent mesoscale and synoptic-scale circulations?
What are the impact of canyon flows and other terrain-circulations on ozone and precursor transport along the Wasatch Front?
To what extent did the regional transport of wildfire smoke and its impacts on particulate concentrations affect ozone production?
Notes: We have a lot of data. Still trying to sift through everything.

## Slide 24: Acknowledgements
Funding provided by the Utah Division of Air Quality
Field study participants:
UofU: Luke Leclair-Marzolf, Will Howard, Jeff Jenkins, Allyson Dugan, Sebastian Hoch, Susan Bush, Xia Dong, Nola Lucke, Taylor McCorkle, Dillon Ulrich, Tom Gowan, Chris Galli, Fahad Alotaibi
DAQ: Seth Arnes, Munkh Baassandorj
USU: Randy Martin and group
WSU: John Sohl and group

## Slide 25: Objective analyses of ozone and wind near the surface: 18 June. Impact of lake breeze
Case discussed further in the next talk by Brian Blaylock
Here: 1 km horizontal resolution surface analyses of ozone and vector wind
Noon MDT
18 June

## Slide 26: Objective analyses of ozone and wind near the surface: 18 June. Impact of lake breeze
1:00 PM MDT
18 June
Ca

## Slide 27: Objective analyses of ozone and wind near the surface: 18 June. Impact of lake breeze
2:00 PM MDT
18 June
Case

## Slide 28: Objective analyses of ozone and wind near the surface: 18 June. Impact of lake breeze
3:00 PM MDT
18 June
Case

## Slide 29: Objective analyses of ozone and wind near the surface: 18 June. Impact of lake breeze
4:00 PM MDT
18 June
Case

## Slide 30: Objective analyses of ozone and wind near the surface: 18 June. Impact of lake breeze
5:00 PM MDT
18 June
Case

## Slide 31: Objective analyses of ozone and wind near the surface: 18 June. Impact of lake breeze
6:00 PM MDT
18 June
Case

## Slide 32: Objective analyses of ozone and wind near the surface: 18 June. Impact of lake breeze
7:00 PM MDT
18 June
Case