## Slide 1
Using a Quadcopter as a Near-Surface Observing Platform
Christopher S. Foster (chris.foster@utah.edu), Alex Jacques, Matt Lammers, and John D. Horel
Department of Atmospheric Sciences, University of Utah
Test Flights: Data, Results, and Imagery
Motivation
Summary and UAV Issues
Objective: Evaluate cost-effective options for sampling the boundary layer in basins and valleys for air quality applications
Near-surface vertical profiles of temperature, moisture, and trace gas concentrations in the boundary layer often contain complex structures that vary in space and time and are poorly resolved by balloon or tether sondes
A sonde mounted on a quadcopter provides the capability to control the monitoring of near-surface conditions continuously for 20-30 min flights
Quadcopter Specifications
Charge all batteries before flights
Mount batteries and Windsond to the copter
Test the copter for balance to ensure optimum flight time and stability
Turn on sonde and Windsond software; sonde automatically connects and will acquire GPS
Turn on GoPro and check settings to capture video during flight
Turn on copter transmitter and copter and wait to acquire GPS and transmitter signals
Fly!
Total prep time (outside of charging): ~10 min
Future Work
    Both summer and winter periods are of interest, but each presents its own variety of issues
Potentially use other instrumentation packages:
    Ozonesonde
    Arduino or Rasberry PI sensor systems
Acknowledgements
To download a copy of this poster, please feel free to scan the following code provided here:
Captures surface layer fluctuations well (ascent/descent provides repeated readings at same levels)
    Windsond sensors and software are easy to use with generally reliable communications
    Controlled sampling allows for collection of both vertical and horizontal profiles of temperatures, moisture, pressure, trace gas concentrations, etc.
Deployment Procedure
    We’d like to thank Stephan de Wekker, University of Virginia, for his insight on the FAA Concept of Operations Approval process
    We’d also like to thank Kiwi-Embedded and Anders Petersson for his development of the Windsond instrument system and software
UAV Issues:
Requires obtaining Concept of Operations Approval from the FAA, which is difficult to obtain at the present time
FAA rules are changing within the next 6 months
Goal is to fly next summer and sample meteorological and air quality conditions
Instrument Limitations
    Sensor response slow when rising/falling quickly
    Apparent hysteresis problems
    No valid wind measurements
Quadcopter Limitations
    Short flight time
    VFR conditions only
    No precipitation
    Low wind speeds
##
Current Instrumentation
Kiwi Embedded Windsond
  Sensirion SHT25 Temperature/RH Sensor
  On-board pressure sensor
  Real-time GPS and met data available via radio
The quadcopter and sonde only require two people to operate
Build: | Carbon Fiber
Navigation: | DJI Naza-M V2 GPS
Imaging: | GoPro Camera Mount
Payload Weight: | 1-1.5 kg (~2-3 pounds)
Flight Time: | ~20 min, depending on wind/stress
Max Winds: | 10-15 m/s
Power Source: | 6-Cell LiPo battery
31 Mar 2014
8 Apr 2014
3 Apr 2014
Date/Time | Location | Conditions/Goals
23 Mar 2014 Noon MDT | William Browning Building (WBB) | Clear skies and slightly breezy. Initial test of vertical profile procedure and equipment.
31 Mar 2014 715 AM MDT | Mountain Meteorology Lab (MML) | Clear skies with fresh snow cover. Attempted to capture morning PBL transition before and after sunrise.
3 Apr 2014 630 PM MDT | Mountain Meteorology Lab (MML) | Mostly cloudy with convective showers dissipating. Attempted to capture evening PBL transition/canyon drainage.
8 Apr 2014 630 PM MDT | Mountain Meteorology Lab (MML) | Very warm with some high cirrus cloud. Attempted to capture evening PBL transition/canyon drainage.
Potential Time Response and/or Hysteresis Issues
GoProTM Imagery and Data from Flights
QR CODE