## Slide 1
2013 Uintah Basin Winter Ozone Study
http://www.deq.utah.gov/locations/
uintahbasin/studies/UBOS-2013.htm
John Horel and Erik Crosman
Mountain Meteorology Group
Department of Atmospheric Sciences
University of Utah
john.horel@utah.edu
erik.crosman@utah.edu

## Slide 2
2013 Uintah Basin Winter Ozone Study
Researchers From:
Utah State University
National Oceanic and Atmospheric Administration
Utah Department of Environmental Quality
University of Utah
University of Colorado, Boulder
University of Wyoming
University of California Los Angeles
University of Washington
See report for researchers’ contact info
http://www.deq.utah.gov/locations/
uintahbasin/studies/UBOS-2013.htm

## Slide 3
2013 Uintah Basin Winter Ozone Study
Funding:
Uintah Impact Mitigation Special Service District
Western Energy Alliance
Questar Energy Products
Bureau of Land Management
National Oceanic and Atmospheric Administration
Environmental Protection Agency
Utah Department of Environmental Quality
Utah Science Technology and Research Initiative
Utah School and Institutional Trust Lands Administration

## Slide 4
2013 Uintah Basin Winter Ozone Study
Background
Current EPA standard: 75 ppb
First measured elevated ozone: 2009
First extensive study: 2011
Ongoing field campaigns: 2012-2014
http://www.deq.utah.gov/locations/
uintahbasin/studies/UBOS-2013.htm

## Slide 5
2013 Uintah Basin Winter Ozone Study
Takeaway Points
Oil and gas production is large and growing
Production releases particulates and array of gases
When snow on ground and stable atmosphere, ozone generated photo-chemically and trapped near ground
Key unknowns:
  Emissions
  Role of ozone precursor gases, such as nitrous acid and formaldehyde
http://www.deq.utah.gov/locations/
uintahbasin/studies/UBOS-2013.htm

## Slide 6
Simulation of a Cold-Air Pool and Winter Ozone Episode in Utah’s Uintah Basin
E. Neemann, E. Crosman, J. Horel, L. Avey
Atmospheric Chemistry and Physics To be submitted
1 Feb
2 Feb
6 Feb
4 Feb
3 Feb
5 Feb
2014

## Slide 7
Background - Ozone & Health
U.S. EPA: http://www.epa.gov/apti/ozonehealth/population.html
Surface ozone is a significant health hazard to humans
Respiratory irritation and inflammation
Aggravated asthma
Long-term lung damage
Increased hospital admissions
and ER visits
Increased mortality

## Slide 8
Winter Ozone Production
q
Z
NOx
Snow Cover
VOCs
O3
Oil and gas operations release ozone precursors: volatile organic compounds (VOCs) and nitrous oxides (NOx)
Pollutants trapped near surface when stable conditions aloft
Snow cover sustains cold air near surface
High albedo snow reflects sunlight back to atmosphere enhancing photochemical reactions with ozone precursors
Leads to elevated ozone levels trapped near the surface
(Precursors)O + h O
O + O2 O3

## Slide 9: Increase in Oil and Gas Drilling in Utah

## Slide 10
9,400 oil & gas producing wells in March 2014
Over 3,600 permits for additional wells since Jan 2012
Uintah Basin
Courtesy of Utah Division of Oil, Gas, and Mining

## Slide 11
Emissions (Barickman 2014)
Emission inventories for the Basin remain incomplete
Difficult to obtain emissions data due to diverse surface and mineral rights
VOC emissions depend on well and equipment types
Inventory data specific to winter ozone season needed as emissions from evaporation ponds and methanol uses have large seasonal variations

## Slide 12: Volatile Organic Compound (VOCs) by Hydroxyl (OH) reactivity measured during UBOS 2013
Roberts et al. (2014)

## Slide 13
Duchesne
River
Green
River
White
River
Mobile Ozone Transect - 6 Feb 2013
High concentrations measured throughout the basin
Greatest values in lower elevations and river valleys
NAAQS
Vernal
Roosevelt
Ouray

## Slide 14
Atmospheric Stability Aloft Traps Pollutants
Photos: Erik Crosman
1-6 Feb 2013: Backscatter and Estimated Aerosol Depth
CLEAN AIR
POLLUTED LAYER
Elevation (m)
Time ->
Temp
Dewpoint
WARM
FOG/LOW CLOUDS
COLD

## Slide 15: Karion et al. (2014)
Figure 4-13. Profiles of constituents measured on the aircraft on January 31 in the vicinity of the natural gas field and gas processing plants.
Temp
OZONE

## Slide 16: Current EPA ozone standard violated if:
3-yr average of the annual calendar year 4th highest daily max 8-hr average exceeds 75 ppb
Ozone levels in Uintah Basin over past 5 winters:
  2010 2011 2012 2013 2014

## Slide 17: Current EPA ozone standard violated if:
3-yr average of the annual calendar year 4th highest daily max 8-hr average exceeds 75 ppb
Ozone levels in Uintah Basin over past 5 winters:
  2010 2011 2012 2013 2014
Above
Above
Above
Below
Below

## Slide 18: Current EPA ozone standard violated if:
SNOW: red
NO SNOW: cyan
CLOUDS: white
3-yr average of the annual calendar year 4th highest daily max 8-hr average exceeds 75 ppb
Ozone levels in Uintah Basin over past 5 winters:
  2010 2011 2012 2013 2014
Which is largely controlled by extent of snow cover in basin:
Wide
Wide
Wide
Little
Little
2 Feb 2013
21 Feb 2014
Above
Above
Above
Below
Below

## Slide 19: Schnell et al. (2014)

## Slide 20
Snow in the Uintah Basin
It doesn’t snow often and, when it does, it usually doesn’t snow much
Stable, stagnant conditions inhibit ablation (ice -> vapor)
Fog/low clouds reflect water cycling: ice-> vapor -> cloud -> snow via deposition/riming
Albedo can remain high due to metamorphism of snow pack over time
Complex chemistry happening with ozone precursors in the snow pack
Photo: Erik Crosman

## Slide 21
What If? Simulation of Mean Afternoon Ozone
1100 - 1700 LST 1-6 February 2013
SNOW
NO SNOW
2.6
3.0
2.2
1.8
2.4
2.8
2.0
1.6
Height (km)
1.4
1.2
2.6
3.0
2.2
1.8
2.4
2.8
2.0
1.6
Height (km)
1.4
1.2
100
90
80
30
40
50
70
60
ppb
Ozone concentrations notably higher in numerical simulation with SNOW cover
From Neemann, Crosman, Horel, Avey (2014)
Wasatch
Green River
Wasatch
Green River

## Slide 22
2013 Uintah Basin Winter Ozone Study
Takeaway Points
Oil and gas production is large and growing
Production releases particulates and array of gases
When snow on ground and stable atmosphere, ozone generated photo-chemically and trapped near ground
Key unknowns:
  Emissions
  Role of ozone precursor gases, such as nitrous acid and formaldehyde
http://www.deq.utah.gov/locations/
uintahbasin/studies/UBOS-2013.htm

## Slide 23
2013 Uintah Basin Winter Ozone Study
Developing Control Strategies
Episodic or seasonal controls may be appropriate for winter ozone concerns
Emission reductions at Bonanza power plant are unlikely to have any effect on winter ozone episodes
Reductions in all VOC emissions will be beneficial
reductions in formaldehyde and aromatic VOC will be more beneficial on a per ton basis; however, less reactive VOCs dominate emissions and ozone production
Personal opinion: business as usual is not an option…
Uintah Basin Standard

## Slide 24: Collaborations Involving UU
State of Utah Energy Initiatives and Imperatives Program:
  Computer Modeling of Winter Ozone Formation in the Uintah Basin
  M. Mansfield (USU), J. Horel ( UU), S. Lyman (USU), J. Hansen (BYU) (1-year project)
NOAA:
  The Uintah Basin Greenhouse Gas Study: Understanding emissions of CO2 and CH4 from oil and gas fields
  J. Lin, J. Horel, J. Ehleringer (3-year project)