## Slide 1
USArray TA Surface Pressure Observations within the Atmospheric Science Community
Alexander A. Jacques, John D. Horel, and Erik T. Crosman
Department of Atmospheric Sciences, University of Utah
Plenary Session II: From Groundwater to the Ionosphere
Earthscope National Meeting 2015
Stowe, VT
June 15, 2015

## Slide 2
Introduction
Early 2012: MesoWest research group at Univ. of Utah contacted by IRIS about surface pressure data available from USArray TA
    March 2012: automated procedures put in place to acquire real-time data from IRIS and store in MesoWest
    Ingest code still running for TA, CEUSN, and Alaska stations
Collaboration with Dr. Frank Vernon (co-PI) led to NSF proposal to further research 1 Hz sampled surface pressure observations with respect to atmospheric phenomena
Jacques, A. A., J. D. Horel, E. T. Crosman, and F. L. Vernon, 2015: Central and Eastern United States Surface Pressure Variations Derived from the USArray Network. Monthly Weather Review, 143, 1472-1493, doi:10.1175/MWR-D-14-00274.1

## Slide 3
What is MesoWest? (http://mesowest.utah.edu)
Ongoing project with National Weather Service to collect and disseminate surface observations from various “mesonets”
    Aviation, fire weather, road weather, public, research, etc.
    28,521 active stations reporting as of 1 June 2015
Stowe, VT

## Slide 4
USArray TA and MesoWest (http://mesowest.utah.edu)
1 Hz surface pressure observations collected from IRIS
    5 minute averages produced to satisfy real-time data needs
    Other atmospheric data also collected for TA-Inframet sites

## Slide 5
MesoWest data disseminated to NWS Western Region and NOAA Meteorological Automated Data Ingest System (MADIS), which sends to National Centers for Environmental Prediction (NCEP)
http://preview.weather.gov/edd
https://madis-data.ncep.noaa.gov/MadisSurface/
USArray TA and MesoWest (http://mesowest.utah.edu)

## Slide 6
USArray TA Observations for Research Activities
Additional processing collects 1 Hz surface pressure data on a daily basis and archives in compressed HDF5 format for quick access
Web tools also developed (http://meso1.chpc.utah.edu/usarray)
Pressure Perturbation Maps
1 Hz and Filtered Perturbation Time Series
TA-BGNE

## Slide 7
Pressure Time Series Analyses
Band-pass filters applied to extract perturbations of interest at several different scales of phenomena (Jacques et al. 2015)
1 Hz
Actual Observations
Synoptic
(30 h – 5 days)
High/low pressure
systems, blizzards
Sub-synoptic
(4 – 30 h)
Diurnal fluctuations,
fronts, some convection
Mesoscale
(10 min – 4 h)
Thunderstorm complexes,
gravity waves

## Slide 8
Perturbation “climatologies” provide additional geographical and seasonal information on occurrences of high-impact phenomena
Pressure Time Series Analyses
Mesoscale Perturbations (per season) > 3 hPa in Magnitude
Winter
Summer
Spring
Autumn

## Slide 9
Web tools provide ability to examine individual events
Pressure Time Series Analyses
Synoptic Filtered Pressure Falls > 24 hPa/day from 1 Jan 2010 – 28 Feb 2014

## Slide 10
Web tools provide ability to examine individual events
Pressure Time Series Analyses
Synoptic Filtered Pressure Falls > 24 hPa/day from 1 Jan 2010 – 28 Feb 2014

## Slide 11
Web tools provide ability to examine individual events
Pressure Time Series Analyses
Synoptic Filtered Pressure Falls > 24 hPa/day from 1 Jan 2010 – 28 Feb 2014

## Slide 12
Spatial Perturbation Analyses
Inclusion of USArray TA observations (high temporal resolution) with gridded model data (high spatial resolution) may improve evaluation of perturbations
University of Utah Two-Dimensional Variational Analysis (UU2DVAR)
    Start with gridded data that represents “background”
    Collect observations independent of background
    Assume background and observation error covariances
    Use 2D variational approach to map observations onto background to produce an analysis grid
Further information on UU2DVAR described by Tyndall and Horel (2013)

## Slide 13
Spatial Perturbation Analyses
Prior to analysis, hourly background grids interpolated every 5 min to better utilize temporal resolution of USArray TA
Grids and observations converted to 1 hour pressure tendency (avoids any elevation conflicts between model terrain and station elevation)
UU2DVAR analysis performed on 1 hour tendency data and final analysis grid converted to altimeter setting (sea-level pressure)
Analysis grid time series are band-pass filtered (10 min – 8 h) to better identify perturbations produced by primarily mesoscale processes

## Slide 14
Spatial Perturbation Analyses

## Slide 15
Spatial Perturbation Identification
Work underway to develop and test several algorithms to identify large perturbation features within the filtered analysis grids

## Slide 16
Spatial Perturbation Identification

## Slide 17
Acknowledgements and References
This research is funded by National Science Foundation Grant Number 1252315. We would like to thank Dr. Frank Vernon of Scripps Institution of Oceanography, the USArray Array Network Facility (ANF), and the Incorporated Research Institutions for Seismology (IRIS) for providing access to live data streams for the USArray project. We would also like to acknowledge the Center for High Performance Computing (CHPC) at the University of Utah.
Jacques, A. A., J. D. Horel, E. T. Crosman, and F. L. Vernon, 2015: Central and Eastern United States Surface Pressure Variations Derived from the USArray Network. Monthly Weather Review, 143, 1472-1493, doi:10.1175/MWR-D-14-00274.1
Tyndall, D., and J. Horel, 2013: Impacts of mesonet observations on meteorological surface analyses. Wea. Forecasting, 28, 254-269, doi:10.1175/WAF-D-12-00027.1.