## Slide 1: Uintah Basin WRF Testing
Erik Neemann
20 Sep 2013

## Slide 2
Overview
Description of WRF Setup & Microphysics edits
Explanation of WRF edits
Reasoning for Microphysics edits
General Results
Examples of simulation differences
Errors, Time Series plots, & Vertical profiles
Conclusions

## Slide 3
Summary of Recent WRF Testing & Modifications
Idealized snow cover in Uintah Basin and mountains
Initialized colder skin temperature in the Uintah Basin
Updated land use data to NLCD 2006
Modified VEGPARM.TBL
Snow albedo changes
Edited relative humidity in NAM input files
Microphysics modifications (Thompson)
  Changes to homogeneous freezing temperature
  Changes to ice nucleation temperature
  Turning off cloud ice sedimentation
  Turning off cloud ice autoconversion to snow

## Slide 4
17 cm
22 to 28 cm
(overestimation inside Uintah Basin)
Idealized snow cover in Uintah Basin and mountains
Elevation-dependent snow cover above 2380 m (17 cm to 1 m above 2900 m)
Uniform snow in basin (17 cm depth, 21.25 kg/m3 SWE, 8:1 ratio)
00Z 1 Feb 2013
Domain 3 Modified Snow Cover
00Z 1 Feb 2013
NAM Analysis Snow Cover

## Slide 5
Initialized colder skin temperature in Uintah Basin
Initialized skin temperature to 262 K in the basin (below 2380 m)
00Z 1 Feb 2013
Modified Skin Temperaure
00Z 1 Feb 2013
NAM Analysis Skin Temperature
262 K
267 to 268 K

## Slide 6
Updated Land Use data
Updated land use data to NLCD 2006 (1 arc-second)
Uintah Basin primary “shrubland” and “cropland/grassland mosaic”
  “Barren or sparsely vegetated”, “grassland”, and “irrigated cropland & pasture” significantly decreased
262 K
267 to 268 K
New NLCD 2006 data
Old USGS Land Use data
More urban categories
Changes in Uintah Basin

## Slide 7
Modified VEGPARM.TBL
Modified VEGPARM.TBL “SNUP” to 0.02 for vegetation categories 5 & 8 (cropland/grassland mosaic & shrubland)
  Allows 2 cm of SWE (20 kg/m3) to “cover up” vegetation with snow
  Enables albedo to attain “max snow albedo”, instead of combination of snow albedo and vegetation albedo
Changed from .04 to .02
Changed from .03 to .02

## Slide 8
0.82
0.76
0.72
0.76
Snow Albedo changes
Combination of VEGPARM.TBL and snow albedo edits achieved desire albedos
Set snow albedo to 0.82 within the basin (below 2380 m)
Set snow albedo to 0.71 outside the basin within domain 2
New snow albedo edits
(0.82 in Basin, 0.71 outer box)
Original snow albedo edits
(0.71 everywhere)
*Note: color scale are different

## Slide 9
Edited RH in NAM input files
Crudely subtracted 5, 20, or 40% from RH in NAM input files
Reduced RH by fraction if already very low to prevent negative values
00Z 1 Feb 2013
Edited NAM RH reduced 20 %
00Z 1 Feb 2013
Original NAM RH

## Slide 10
Edited RH in NAM input files - Integrated clouds hydrometeors
Reduced RH decreased clouds earlier in simulation (1-2 days)
All simulations converged on very similar cloudy solution after first couple days
Thompson 1.33km
Thompson 4km RH-5%
Thompson 4km RH-20%
15Z 1 Feb 2013
15Z 5 Feb 2013

## Slide 11
Reasoning for Microphysics Modifications
Several modification were made to Thompson microphysics schemes:
  Changes to homogeneous freezing temperature (HGFR) from 235 to 271 K
    Desired effect of changing liquid clouds to ice clouds
  Changes to ice nucleation temperature from -12 to range of -3 to -15 C
    Desired same effect as changing homogeneous freezing temperature, but more physically realistic
  Turning off cloud ice sedimentation
    Effort to prevent cloud ice from “falling out” of cloud
  Turning off cloud ice autoconversion to snow
    Effort to maintain cloud ice by preventing it’s conversion into snow category and precipitating out of cloud
Modifications were conducted in various combinations to determine impact on model simulations
In final tests, modifications were then only allowed in lowest 15 model levels (~500 m), while everything above was unchanged
  Effort to create more realistic simulation by only changing low levels

## Slide 12
General Results of Microphysics Modifications
Combination of edits seemed to converge on 3 solutions:
  1 - “clear sky” solution with very little cloud ice and negligible LW radiation
    Simulations where ice clouds were created and:
      Ice autoconversion to snow was ON
      Autoconversion OFF, but sedimentation of cloud ice ON
  2 - “thick ice cloud” solution with moderate LW radiation
    Simulations where ice clouds were created and:
      Both autoconversion and sedimentation were OFF
  3 - “thick liquid cloud” solution with strong LW radiation when:
    No microphysics edits
    Simulations where ice clouds were created via ice nucleation:
      Either sedimentation or autoconversion was ON

## Slide 13
Integrated Clouds
TIAU0
09Z 3 Feb 2013
TIAU0
TS20IAU0
Cloud Ice bottom 10 levels
TS20IAU0
Microphysics Modifications - Cloud Ice sedimentation

## Slide 14
Microphysics Modifications - Sedimentation and Autoconversion
TFSCA
WSM3A
TIAU0
TIAU20
TIAU5
TSIAU0
Cloud ice bottom 10 levels - 06Z 4 Feb 2013

## Slide 15
Microphysics Modifications - Sedimentation and Autoconversion
Sedimentation OFF,
Autoconversion ON
WSM3 Microphysics
Sedimentation OFF,
Autoconversion OFF
Sedimentation OFF,
20% Autoconversion
Sedimentation OFF,
5% Autoconversion
Sedimentation ON,
Autoconversion OFF
Cloud ice bottom 10 levels - 4 Feb 2013 06Z

## Slide 16
Effect of Sedimentation on 2m Temps, Clouds, LW Radiation
2m Temps
Integrated Clouds
06Z 4 Feb 2013
LW Radiation at sfc
2m Temps
Integrated Clouds
LW Radiation at sfc
TIN3IAU0 - Ice sedimentation OFF
TSIN3IAU0 - Ice sedimentation ON

## Slide 17
Sedimentation - Average cloud ice & cloud water bottom 10 levels
TIN3IAU0
- Ice sedimentation OFF
Cloud Ice
06Z 4 Feb 2013
TSIN3IAU0
- Ice sedimentation ON
Cloud Water
Cloud Ice
Cloud Water

## Slide 18
Uintah Basin CAP Simulation 1-6 Feb 2013
Distribution of cloud ice with and without sedimentation
QSNOW 6.6x10-3
QICE 5.6x10-4
TIN3IAU0
TSIN3IAU0
Allowing cloud ice sedimentation in low levels resulted in a liquid-phase dominated cloud
Both cases had essentially identical results above 2-3 km
QCLOUD 0.045 g/kg
QICE 0.11 g/kg

## Slide 19
Mean Errors:
Original Thomp 4km = 3.5576 C
WSM3 0.82 alb 4km = 1.9254 C
Thomp RH-40%, 0.82 alb = 2.9908 C
Thomp 300 CCN 0.82 alb = 1.3055 C
Thomp ice, fall speed zero = 3.0842 C
Thomp ice, FS=0, 300 CCN, alb = -0.75 C
Uintah Basin CAP Simulation 1-6 Feb 2013
“thick liquid cloud”
“thick ice cloud”
“clear sky”

## Slide 20
Mean Abs Errors:
Original Thomp 4km = 3.9772 C
WSM3 0.82 alb 4km = 2.5456 C
Thomp RH-40%, 0.82 alb = 2.6232 C
Thomp 300 CCN 0.82 alb = 3.1315 C
Thomp ice, fall speed zero = 3.4003 C
Thomp ice, FS=0, 300 CCN, alb = 3.9772 C
Uintah Basin CAP Simulation 1-6 Feb 2013

## Slide 21
RMSE:
Original Thomp 4km = 4.7447 C
WSM3 0.82 alb 4km = 3.1065 C
Thomp RH-40%, 0.82 alb = 3.2344 C
Thomp 300 CCN 0.82 alb = 3.8061 C
Thomp ice, fall speed zero = 3.9650 C
Thomp ice, FS=0, 300 CCN, alb = 2.5162 C
Uintah Basin CAP Simulation 1-6 Feb 2013

## Slide 22
2m Temperature Errors for all runs and accumulated snow at Ouray
Thompson runs with HGFR temp = 271.15
WSM3 runs
Thompson runs with reduced RH in boundary conditions
No tweaks to microphysics (Thompson & Morrison)
Thompson runs with different cloud droplet concentrations
Thompson runs with ice nucleation changes in bottom 15 model levels

## Slide 23
Uintah Basin CAP Simulation 1-6 Feb 2013

## Slide 24
Uintah Basin CAP Simulation 1-6 Feb 2013

## Slide 25
Uintah Basin CAP Simulation 1-6 Feb 2013

## Slide 26
Uintah Basin CAP Simulation 1-6 Feb 2013

## Slide 27
1 Feb 2013
2 Feb 2013
3 Feb 2013
4 Feb 2013
5 Feb 2013
6 Feb 2013
18Z Roosevelt

## Slide 28
1 Feb 2013
2 Feb 2013
3 Feb 2013
4 Feb 2013
5 Feb 2013
6 Feb 2013
12Z Horsepool

## Slide 29
1 Feb 2013
2 Feb 2013
3 Feb 2013
4 Feb 2013
5 Feb 2013
6 Feb 2013
12Z Ouray

## Slide 30
1 Feb 2013
2 Feb 2013
3 Feb 2013
4 Feb 2013
5 Feb 2013
6 Feb 2013
12Z Red Wash

## Slide 31
Conclusions
Preferred WRF run and edits (TIN12IAU0)
  Include idealized snow cover, albedo, skin temperature, updated land use, and edited VEGPARM.TBL
  Do not edit RH in NAM initialization/boundary condition files
  Only make microphysics edits in lowest 15 model levels
  Leave ice nucleation at default temperature of -12 C
  Turn off autoconversion and sedimentation in bottom 15 model levels
Preferred setup results in:
  Ice-phase clouds in place of original liquid-phase cloud
  Colder surface temperatures with smaller errors/bias
  More physically representative radiative properties of ice-phase cloud
  Shallower PBL that more closely matches observed soundings